## Slide 1
Optimal control of a 1D diffusion process with a team of mobile actuators under jointly optimal guidance
Sheng Cheng and Derek A. Paley
University of Maryland
American Control Conference
July 2, 2020
Notes: \

## Slide 2: Motivation
Source: www.bloomberg.com
Monitoring and control of a large-scale spatiotemporal process is dangerous and costly when conducted by humans.
Autonomous vehicles substitute human operators when
  equipped with sensors and actuators
  guided under designated control policy
Source: offshore-technology.com
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Introduction
Formulation
Solution method
Summary
Source: fireaviation.com

## Slide 3
Relation to prior work and contributions
Actuator type |  | Representative work | Approach
 | Boundary | [Smyshlyaev and Krstic, 2010] | Backstepping
 |  | [Morris, 2010] | LQ
Stationary | In-domain | [Morris et al., 2010] | H2
 |  | [Demetriou, 2017] | Maximum controllability
Mobile |  | [Demetriou et al., 2003] | LQ
 |  | [Xue and El-Farra, 2018] | LQ
 |  | [Demetriou, 2010] | Lyapunov-based methods
 |  | [Demetriou, 2012] | Lyapunov-based methods
 |  | [Chen et al., 2005] | Centroidal Voronoi tessellation
Contributions of paper:
  Formulate an integrated optimization problem to control a PDE with mobile actuators
  Show conditions under which optimal guidance restricts the actuators in-domain
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Introduction
Formulation
Solution method
Summary
Notes: [Demetriou et al., 2003]: LQ cost with discretized actuator location. The optimization is LQR with infinite horizon
[Xue and El-Farra, 2018]: LQ cost with penalty on sensor-controller communication cost

## Slide 4
Infinite-dimensional system: LQR
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Consider a 1D diffusion equation with known initial condition and zero Dirichlet boundary condition:
Assume linear and first-order dynamics of the mobile actuators
Abstract linear system representation [Curtain and Zwart, 1995]
position
guidance
PDE state
control
Dirac delta
Amplitude
Introduction
Formulation
Solution method
Summary
Notes: Label y axis

## Slide 5
Infinite-dimensional system: LQR (cont.)
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Abstract linear system representation of a PDE
Linear-quadratic regulator formulation
Linear-quadratic optimal control:
with operator-valued differential Riccati equation [Bensoussan et al. 2007]:
state cost
control effort
terminal state cost
Introduction
Formulation
Solution method
Summary

## Slide 6
Introduction
Formulation
Solution method
Summary
Problem formulation
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Find actuation control and actuator guidance that solve
with
PDE-related cost
Mobility-related cost

## Slide 7
Introduction
Formulation
Solution method
Summary
Optimal guidance: Actuators stay in domain
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Problem (P) does not have an explicit constraint on actuators staying within the spatial domain.
An optimal guidance will guarantee the actuators to stay within the spatial domain under certain conditions.
☹️
🙂
Notes: Remove last comma

## Slide 8
Optimal guidance: Actuator stay in domain (cont.)
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Theorem Consider problem (P) with the following assumptions:
Single integrator dynamics of the actuators:
State running cost of the actuators is zero:
Initial locations of the actuators are in domain:
Either, terminal locations are in domain:
or, no terminal cost for the actuators:
Then, any guidance that steers the mobile actuators out of the domain is not optimal.
Sketch of proof:
Start with arbitrary guidance that steers one actuator outside the domain.
Construct the second guidance that always restricts the actuator in the domain using first guidance.
The second guidance always incurs smaller cost than the first guidance.
Introduction
Formulation
Solution method
Summary

## Slide 9
Solution method: Approximated problem
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Galerkin approximation
Consider the approximated version of the problem:
with approximated PDE-related cost
(P1-A) is not an LQR: is a nonlinear function of .
Introduction
Formulation
Solution method
Summary

## Slide 10
Solution method: Pontryagin’s maximum principle
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Hamiltonian:
co-state dynamics
terminal conditions
optimality conditions
Introduction
Formulation
Solution method
Summary
Notes: Remove commas

## Slide 11
Solutions: open-loop vs. feedback control
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Feedback control synthesized using LQR:
Original problem (P)
Approximated problem (AP)
Optimal open-loop guidance
Optimal open-loop control
Optimal trajectory
Optimal feedback control
Galerkin approximation
PMP
LQR of
PDE
Introduction
Formulation
Solution method
Summary

## Slide 12
Numerical example
Four mobile actuators：
  initiated at one location
  evenly spaced terminal locations.
Feedback control synthesized using LQR
Comparison groups:
Name | Control and guidance
Optimal feedback | Optimal feedback control with optimal open-loop guidance
Optimal open-loop | Optimal open-loop control with optimal open-loop guidance
Semi-naive | Output feedback control with optimal open-loop guidance
Naive | Output feedback control with constant speed guidance
Introduction
Formulation
Solution method
Summary
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Notes: Label y axis of animation
2 slides: explain the comparison
animation on left and figures on right (second page)

## Slide 13
Numerical example (cont.)
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Introduction
Formulation
Solution method
Summary
Notes: Label y axis of animation
2 slides: explain the comparison
animation on left and figures on right (second page)

## Slide 14
Summary and ongoing work
Sheng Cheng and Derek A. Paley
American Control Conference 2020
Optimal control of a diffusion process using a team of mobile actuators under jointly optimal guidance
Ongoing work
  Extend the framework to diffusion-advection process with 2D spatial domain
  More efficient numerical computation
  Convergence of the solution of the approximated problem (AP)
  Simultaneous estimation and control with a team of mobile sensor-plus-actuators.
Introduction
Formulation
Solution method
Summary
Notes: Add slides (1-3) with details on Ongoing work

## Slide 15
Thank you!
Sheng Cheng and Derek A. Paley
American Control Conference 2020
This work is supported by DARPA Contract No. HR001118C0142
cheng@terpmail.umd.edu
Introduction
Formulation
Solution method
Summary